## Slide 1: OSED EVALUATION
NAME | USN | ROLL NUMBER
Rahul RC | 01FE20BEC210 | 426
Sneha GH | 01FE20BEC209 | 425
Neyush Mohta | 01FE20BEC213 | 429
Sagar CK | 01FE20BEC206 | 422

## Slide 2: PROBLEM STATEMENT
->An equipment in an industry continuously monitors the temperature to open or close a valve to the air conditioner. Realize the system.

## Slide 3: BLOCK DIAGRAM
LPC2148
Start Task1
Read ADC_Value
Send ADC_Valueto MessageBox
Maliboox_Define
UART0_Initialize
Display Temperature on UART0
Check if Temperature greater than threshold
Run Motor
If True?

## Slide 4: ALGORITHM
START.
MAILBOX IS CREATED
UART0 IS INITIALIZED
MAILBOX IS DEFINED AND INITIALIZED
ADC_VALUE IS READ UNDER TASK 1
SEND THE ADC_VALUE TO MAILBOX
RECEIVE ADC_VALUE FROM MAILBOX IN TASK 2
DISPLAY VALUE ON UART0
BASED ON CONDITION,RUN DC MOTOR

## Slide 5: PIN DETAILS
P0.25 = AD0.4
P0.0 & P0.1 = UART0

## Slide 6: IMPLEMENTATION
#include <rtl.h>
#include <lpc214x.h>
#include <stdio.h>
OS_TID tsk1,tsk2,tsk3; //declare task identification number variables
os_mbx_declare (MsgBox, 100); /* Declare an RTX mailbox 100 msgs with name MsgBox*/
_declare_box(mpool,20,32); /* Reserve a memory for 32 blocks of 20 bytes */
void delay(unsigned long int);
void hascii(int *);
unsigned int adc_value=0,temp_adc=0;
int temp,i;
int var[10];
char val[15];

## Slide 7
void serial()
{
PINSEL0 |= 0x00000005;
U0LCR = 0x83;
U0DLL = 0x61;
U0LCR = 0x03;
U0IER = 0x01;
}
void delay(unsigned long int r1)
{
unsigned long int r;
for(r=0;r<r1;r++);
}
__task void job1 (void); //declare function for job1
__task void job2 (void); //declare function for job2
__task void job3 (void); //declare function for job3

## Slide 8
__task void job1 (void) // job1 function definition
{
U32 *mptr;
os_tsk_prio_self (3); // assign priority to job1 as 2
tsk2=os_tsk_create (job2, 0); //create job2 and keep in ready state
os_mbx_init (MsgBox, sizeof(MsgBox));
mptr = _alloc_box (mpool); /* Allocate a memory for the message */
PINSEL1 |= 0X00040000; //AD0.4 pin is selected(P0.18)
while (1)
{
//CONTROL register for ADC
AD0CR = 0x09200010; //command register for ADC-AD0.4
delay(100);
while((temp_adc = AD0GDR) == 0x80000000); //to check the interrupt bit
adc_value = AD0GDR; //reading the ADC value
adc_value >>=6;
adc_value &= 0x000003ff;
//sprintf(val,"Temperature:%d",adc_value);
sprintf(val,"%d",adc_value);
while (val[i] != '\0')
{
mptr[i] = val[i];
i++;
}
i=0;
os_mbx_send (MsgBox, mptr, 0x00ff);
os_tsk_prio(tsk2,4); //Change priority of task2 to 4
}
}

## Slide 9
__task void job2 (void) // job2 function definition
{
U32 *rptr;
while (1)
{
PINSEL1|=0x00000000;
IODIR0 = 0x00000C00;
IOCLR0 = 0x00000C00;
os_mbx_wait(MsgBox, (void*)&rptr, 0xffff);
while(rptr[i]!='\0')
{
while(!(U1LSR & 0x20));
U0THR = rptr[i]; /* Display the recieved message from UART0 */
i++;
}
i=0;
if(adc_value>0x60)
{
for(i=0;i<10;i++)
{
IOSET0 = 0x00000400;
IOCLR0 = 0x00000800;
delay(500000);
IOSET0 = 0x00000800;
IOCLR0 = 0x00000400;
delay(500000);
}
}
}
}

## Slide 10
int main (void)
{
serial();
os_sys_init(job1); //initialize job1
while (1);
}

## Slide 11: THANK YOU